## Slide 1
The Relevance
of Sediment Regime
for River Ecosystems
Ellen Wohl
Department of Geosciences
Colorado State University
Notes: 25 minutes

## Slide 2
Outline
What is a sediment regime?
How do people alter sediment regimes?
What are the consequences of
altered sediment regimes?
How can a balanced sediment regime be designed?

## Slide 3
I. What is a sediment regime?
Sediment regime includes inputs and outputs of mobile sediment from a length of channel & storage of sediment within the channel and floodplain over a specified time interval.
upstream inputs
suspended load
bed load
downstream outputs
suspended load
bed load
lateral inputs
uplands
tributary
floodplain
banks
lateral outputs
floodplain
banks
storage
floodplain
bed
banks
bars

## Slide 4
Two-part conceptual framework for understanding sediment regimes:
Sediment budget
Water & sediment interactions in a valley context

## Slide 5
Sediment Budget
Basin Scale
(101-106 km2 & 102-106 years)
(climate, geology, land use)
ΔS = Inputs – Outputs + Storage
ΔS = (Ius + Ilat) – (Olat + Ods) + S
Reach Scale
(100-103 m2 & 100-102 years)
(valley geometry, position in basin,
flow regime, river engineering)

## Slide 6
A natural sediment regime is characterized by variations across space & through time.
Mississippi River: space
Sediment discharge
Water discharge

## Slide 7
Bijou Creek, USA: time
braided
meandering

## Slide 8
cross-sectional
geometry
planform
gradient
substrate, hydraulics
resulting spatial heterogeneity in river geometry & connectivity
expressed in the form of spatial variations in channel & floodplain
floodplain
wetlands
inputs
natural flow (Q),
sediment (Qs)
& large wood (LW)
regimes
Q
Qs
LW
time
valley
geometry
&
human
influence
spatial limits on heterogeneity & connectivity
Valley Context

## Slide 9
A natural sediment regime = conditions prior to construction of dams & intensive human disturbance of topography & land cover
Fundamental benchmark for a natural sediment regime:
patterns of ecosystem organization & adaptations of riverine species reflect the spatial pattern & temporal variability of interacting water & sediment regimes

## Slide 10
Flood-pulse model for lowland floodplain rivers
Tagliamento River, Italy
low
flow
flood
flow
mean
flow
Tockner et al., 2000, Hydrological Processes
Bayley et al., 1995, BioScience
Flow-pulse model for braided rivers

## Slide 11
II. How do people alter sediment regimes?
Changes in
flow regime (magnitude, timing, duration)
sediment budget
large wood regime (abundance, distribution)
valley context (channel geometry, connectivity)
Resulting from
land use (land cover, topography)
flow regulation (dams, diversions)
channel engineering
(channelization, bank stabilization, levees, instream mining)

## Slide 12
Example of land use change: urbanization
↓ sediment inputs
↑ water inputs (magnitude, rate of response)
↑ contaminants, ↓ organic matter
Stream response
coarsening of bed sediment
bed & bank erosion
increased flood hazard
reduced water quality
reduced biomass & biodiversity
Notes: Add photos

## Slide 13
Example of flow regulation: dam
↓ downstream sediment flux
∆ flow regime (magnitude, duration, timing, rate of change)
Stream response
coarsening of bed sediment
bed & bank erosion
increased flood hazard
reduced water quality
reduced biomass & biodiversity
Notes: Add photos

## Slide 14
III. What are the consequences of
altered sediment regimes?
Physical: altered channel geometry
Chemical: altered water quality (turbidity, nutrients, heavy metals)
Ecological
declines in habitat (abundance, diversity, stability)
reduced connectivity (channel-floodplain, surface-subsurface)
reduced biodiversity & abundance
Hazards
decreased channel stability (lateral migration, erosion/
aggradation, flooding)
altered downstream fluxes of sediment

## Slide 15
+ sediment
- sediment
+ bed grain size
Δ bed grain size
Δ bedforms
(type, dimension, mobility)
Δ bedforms
(type, dimension, mobility)
bank erosion
aggradation
floodplain aggradation
Δ gradient
Δ planform
Δ planform
incision
Δ gradient
floodplain erosion
Δ habitat, thermal regime
& disturbance regime
Physical
Wohl et al., 2015, BioScience

## Slide 16
Case study
flow regulation & rivers of the US Great Plains
Platte River near Kearney, Nebraska
1938
1988
substantial increase in riparian vegetation (darker gray color) & channel narrowing
habitat loss: endangered fish & bird species
braided
anastomosing

## Slide 17
Case study
dams & the Colorado River ecosystem
pre-dam hydrograph
post-dam hydrograph
experimental flood

## Slide 18
Negative effects of dam
eliminates downstream sediment flux
(importance of tributaries)
alters flow hydrograph
(magnitude & duration of peak, rate change)
changes water thermal regime
(bottom release = cold water)
eliminates longitudinal fish migration & limits use of
floodplain habitat
alters channel-margin habitat
(riparian zone, backwaters)
limits recreational camping sites

## Slide 19
IV. How can a balanced sediment regime
be designed?
A balanced sediment regime = the energy of flow available to transport sediment is in balance with sediment supply:
River form remains dynamically stable over a specified time period.
In a management context, a balanced sediment regime is one that results in a channel that transports the sediment supplied to it with the available flow.

## Slide 20
Key management questions:
What river system structure & function can be achieved under a modified flow regime and balanced sediment regime?
What are the supplies of water and sediment?

## Slide 21
Potential metrics for assessing sediment dynamics
1. Sediment flux
suspended sediment (concentration, grain-size distribution)
bed-material sediment (volume per unit time, grain size)
reservoir sedimentation
sediment balance via CSR or S*
Capacity Supply Ratio (CSR) (Soar & Thorne, 2001)
CSR > 1 erosion
CSR < 1 aggradation

## Slide 22
S* indicator of potential for aggradation or degradation in response to changes in water & sediment supply
(Schmidt & Wilcock, 2008, Water Resources Research)
, ,
sediment grain discharge
supply size
S = slope needed to transport sediment supplied
S* > 1 means increase in S needed to transport post-dam
sediment supply for specified change in flow
S* < 1 means pre-dam S is larger than now needed &
sediment deficit is predicted

## Slide 23
Potential metrics for assessing sediment dynamics
2. Channel geometry
cross-sectional channel geometry (width, depth, bedform type &
dimensions, bank stability, pool volume)
bars & islands (number & successional stages)
bed substrate (grain size distribution, particle stability)
channel planform (sinuosity, number of channels)
floodplain (extent, turnover time, habitat diversity)
3. Vegetation patterns
spatial heterogeneity of species & plant ages

## Slide 24
V. Moving Forward
Current understanding & tools allow us to predict the trajectories of river change in response to changes in sediment regime.
Measures of sediment balance can be used to determine whether the relative sediment supply is increasing or decreasing within a river segment & to assess the magnitude of change.

## Slide 25
These variables can also be used to design management that creates a balanced sediment regime & facilitates channel stability.
A channel in dynamic equilibrium may not necessarily create the desired river system structure & function required to support native biota – channel stability in itself may not always be a sufficient management goal.

## Slide 26
An understanding of sediment regime can be used to manage for a dynamically stable channel in which water and sediment interact to create the habitat & disturbance regime needed to support river biota.
With the tools and understanding currently available, there is no justification for managing river systems without explicitly considering sediment regime & every incentive to do so.